## Slide 1: Zooming in on Wide-area Latencies to a Global Cloud Provider
Yuchen Jin, Sundararajan Renganathan, Ganesh Ananthanarayanan, Junchen Jiang, Venkat Padmanabhan, Manuel Schroder, Matt Calder, Arvind Krishnamurthy

## Slide 2
1. BlameIt: A tool for Internet fault localization to ease the lives of network engineers with automation & hints
2. BlameIt uses a hybrid approach (passive + active)
  Use passive end-to-end measurements as much as possible
  Issue selected active probes for high-priority incidents
3. Production deployment of passive BlameIt at Azure
  Correctly localizes the fault in all 88 incidents with manual reports
  72X lesser probing overhead
TL;DR
When clients experience high Internet latency degradation to cloud services, where does the fault lie?
Cloud services: high latency  lower user engagement 

## Slide 3: Public Internet communication is weak
DC1
edge1
edge2
edge3
Internet segment is the weak link!
(little visibility/control)
Cloud Network
DC2
edge4
Intra-DC and inter-DC communications have seen rapid improvement
Congestions inside/between AS(es)
Path updates inside an AS
AS-level path changes
Maintenance issues in client’s ISP

## Slide 4: When Internet perf is bad (RTT inflates), where in the path is to blame?
Client ISP (e.g., Comcast AS)
Cloud (e.g., Azure, AWS)
Contact ISP if issue is widespread
Re-route around the faulty AS
Contact other AS’s network operations center (NOC)
Problem at cloud end
Investigate server issue
Investigate edge-DC connection

## Slide 5
Passive analysis of end-to-end latency
  Network tomography for connected graphs
  Under-constrained due to insufficient coverage of paths
Active probing for hop-by-hop latencies
  Frequent probes from vantage points worldwide
   Prohibitively expensive at scale
iPlane [OSDI’06], WhyHigh [IMC’09], Trinocular [Sigcomm’13], Sibyl [NSDI’16], Odin [NSDI’18]
When Internet perf is bad (RTT inflates), where in the path is to blame?
Network tomography [JASA’96, Statistical Science’04], Boolean tomography [IMC’10], Ghita et al. [CoNEXT’11], VIA [Sigcomm’16], 007 [NSDI’18]

## Slide 6: BlameIt: A hybrid approach
Coarse-grained blame assignment using passive measurements
CLIENT SEGMENT
MIDDLE SEGMENT
CLOUD SEGMENT
Fine-grained active traceroutes only for (high-priority) middle-segment blames

## Slide 7
Coarse-grained fault localization with passive measurements
Fine-grained localization with active probes
Evaluation
Outline

## Slide 8: Architecture
SYN
SYN/ACK
ACK
Data analytics cluster
TCP handshake
client IP, device type,
timestamp, RTT
Hundreds of edge locations
Hundreds of millions of clients

## Slide 9: Quartet
Quartet: {client IP /24, cloud location, mobile (or) non-mobile device, 5 minute time bucket}
  Better spatial and temporal fidelity
  > 90% quartets have at least 10 RTT samples
  A quartet is “bad” if its average RTT is over the badness threshold
Badness thresholds: RTT targets varying across regions and device connection types.
{10.0.6.2, NYC Cloud, mobile, 02:00:33}: 32ms
{10.0.6.7, NYC Cloud, mobile, 02:02:25}: 34ms
{10.0.6.132, NYC Cloud, mobile, 02:04:49}: 36ms
Quartet:
{10.0.6.0/24,
NYC Cloud,
mobile,
time window=1}
 average RTT: 34ms

## Slide 10: BlameIt for localizing Internet fault
1. Identify “bad” quartets. {IP-/24, cloud location, mobile (or) non-mobile device, time bucket}
2. For each bad quartet,
Start from the cloud, keep passing the blame downstream if no consensus
If (> τ) quartets to the cloud have RTTs > cloud’s expected RTT
Blame the cloud
If (> τ) quartets sharing the middle segment (BGP path) have RTTs > middle’s expected RTT
Blame the middle segment
Good RTT to another cloud
Ambiguous
If not sufficient RTT samples
Insufficient
Else
Blame the client
τ = 80%
NYC
Chicago

## Slide 11: Key empirical observations
Only one AS is usually at fault
  E.g., Either the client or a middle AS is at fault, but not both simultaneously
Smaller “failure set” is more likely than a larger set
  E.g., If all clients connecting to a cloud location see bad RTTs, it’s the cloud’s fault
  (and not all the clients being bad simultaneously)
Hierarchical elimination of the culprit starting with the cloud, and stop when we are sufficiently confident to blame a segment

## Slide 12: Learning cloud/middle expected RTT
Each cloud location’s expected RTT is learnt from previous 14 days’ median RTT
Each middle segment’s expected RTT is learnt from previous 14 days’ median RTT
RTT(ms)
P(RTT)
35
30
40
50
cloud location’s expected RTT is 40ms
> τ (=80%) quartets to the cloud have RTT higher than its expected RTT (40ms)
55

## Slide 13
Coarse-grained fault localization with passive measurements
Fine-grained localization with active probes
Evaluation
Outline

## Slide 14: BlameIt: A hybrid approach
Coarse-grained blame assignment using passive measurements
CLIENT SEGMENT
MIDDLE SEGMENT
CLOUD SEGMENT
Fine-grained active traceroutes only for (high-priority) middle-segment blames

## Slide 15: Approach for localizing middle-segment issues
AS 8075
AS m1
AS m2
AS client
Background traceroute
On-demand traceroute
4ms
6ms
8ms
9ms
4ms
60ms
62ms
64ms
Contribution of AS m1 = 6 – 4 = 2ms
Contribution of AS m1 = 60 – 4 = 56ms
Blame the AS with greatest increase in contribution!
Background traceroute: obtain the picture prior to the fault.
On-demand traceroute: triggered by the passive phase of BlameIt

## Slide 16: Key observations for optimizing probing volume
Internet paths are relatively stable
  Background traceroutes need to be updated only when BGP path changes
Not all middle-segment issues are worth investigating
Prioritize traceroutes for long-standing incidents!
Most issues are fleeting!
> 60% issues last <= 5 mins

## Slide 17: Optimizing background traceroutes
Issued periodically to each BGP path seen from each cloud location
  We keep it to two per day hitting a “sweet spot” of high localization accuracy and low probing overhead
Triggered by BGP churn i.e. BGP path change at border routers
  Whenever AS-level path to a client prefix changes at border routers

## Slide 18
Approximate damage of user experience: number of affected users (distinct IP addresses) X the duration of the RTT degradation
If ranked by client-time product, top 20% middle segments cover 80% damages of all incidents
Concentration of issues
BlameIt uses estimated client-time product to prioritize middle-segment issues
Optimizing on-demand traceroutes
“client-time product”

## Slide 19
Coarse-grained fault localization with passive measurements
Fine-grained localization with active probes
Evaluation
Outline

## Slide 20
Evaluation highlights
We compare the accuracy of BlameIt’s result to 88 incidents in production having labels from manual investigations done by Azure
BlameIt correctly pinned the blame in all the incidents

## Slide 21: Blame assignments in production
Blame assignments worldwide over a month
Cloud segment issues account for <4% of bad quartets
Well maintained by Azure
“Ambiguous” and “Insufficient” have a large fraction
Fractions are generally stable

## Slide 22: Real-world incident: Peering Fault
Monitoring System | Why it didn’t catch the issue? | How BlameIt avoids this problem
Monitors RTTs to Azure in each {AS, metro} | No single {AS, metro} was badly affected though many clients affected countrywide | Goes more fine-grained by using BGP-paths and client IP-/24s
Monitoring System | Why it didn’t catch the issue? | How BlameIt avoids this problem
Users download web objects to measure latency | Deployed conservatively to limit overheads | Passive data used to issue selective active probes
A high-priority latency issue affecting many customers in the US
BlameIt caught it and correctly blamed the middle segment
Issue was due to changes in a peering AS with which Azure peers at multiple locations
(Other) Monitoring Systems | Why didn’t it catch the issue? | How BlameIt succeeded?
Periodic traceroutes from Azure clients | Clients issuing traceroutes weren’t affected (limited number of clients) | Considers all the clients hitting Azure (using passive measurements)
BlameIt is able notice widespread increases in latency without prohibitive overheads

## Slide 23
Central tradeoff: traceroute overhead vs AS-level localization accuracy
Finding the best background traceroute frequency
Experiment setup: Traceroutes from 22 Azure locations to 23,000 BGP prefixes for two weeks
Accuracy metric: Relative localization accuracy with most fine-grained scheme as ground truth
72X cheaper!
Probing scheme can be configured by the operators

## Slide 24
 Ease the work of network engineers with automation & hints to investigate WAN latency degradation
BlameIt Summary
Hybrid (passive + active) approach
Deployment at Azure produces results with high accuracy at low overheads